## Slide 1: INSTITUTIONAL RESEARCH CORE PROGRAM HIGH RESOLUTION IMAGING FACILITY FLUORESCENCE MICROSCOPY
Ed Phillips
Research Associate
(205) 934-1926
ephillips@uab.edu
HRIF Laser Scanning Confocal Microscopes
Systems: Three confocal microscopes for fixed/live cell and tissue imaging.
Capabilities: 4-channel imaging (405/488/561/647 lasers), high-speed resonance scanning (up to 420 fps), perfect focus for timelapse, live cell chamber (CO2/temp control), spectral detection/unmixing, FRAP, FRET, photoactivation, 2D/3D imaging, calcium imaging, colocalization, GaAsP detectors.
CONFOCAL MICROSCOPY
NANOPARTICLE IMAGING SYSTEM
HISTOLOGY & WIDEFIELD FLUORESCENCE
Alexa Mattheyses, PhD, Director
(205) 975-0680
mattheyses@uab.edu
Robert Grabski, PhD
Imaging Specialist (205)-934-7039
rgrabski@uab.edu
Shawn Williams
Imaging Specialist
(205)-934-7403
tzaron@uab.edu
To schedule time on a microscope or to schedule a training session with HRIF specialist, visit us at:
www.uab.edu/HRIF
Widefield
Confocal
SIM
Structured Illumination Microscopy (SIM)
Resolution: Twice the diffraction limit (~115 nm lateral, ~269–300 nm axial).
Capabilities: Enables detailed 3D visualization of intracellular structures in fixed/live cells and tissues, with optical sectioning for higher spatial resolution.
STochastic Optical Reconstruction Microscopy (STORM)
Resolution: Tenfold improvement (~20 nm lateral, ~50 nm axial).
Capabilities: Reconstructs super-resolution 3D images using precise fluorophore localization. Supports multi-color imaging for 2–3 proteins at the nanoscale.
https://www.nikoninstruments.com/Products/Super-resolution/N-STORM-Super-Resolution
Bartle et al. JCS 2016
Stahley et al, JCS 2016
LIGHTSHEET MICROSCOPY
HRIF Sponsors
UAB Institutional Research Core Program (IRCP)
Comprehensive Cancer Center (P30 CA013148)
Lightsheet - S10 OD032341
Veteran’s Administrative Hospital Research Division
Melissa Chimento Associate Director
(205) 934-1926
mchimento@uab.edu
Mouse brain vasculature and mouse aorta imaged at HRIF core facility. Courtesy of Daniel Tyrrell Ph.D.
Lionheart FX Epifluorescence Microscope
Versatility: Compact system supporting basic and advanced imaging techniques.
Capabilities: Live/fixed specimen imaging in chamber slides, dishes, and plates. Offers color/BW brightfield, fluorescence, and phase-contrast imaging.
NS300 Particle/Exosome Analysis System
Capabilities: Visualizes and measures particles (10–2000 nm) in suspension.
Applications: Protein aggregation, exosomes, drug delivery systems, nanomaterial characterization, and fluorescent particle analysis (488 nm excitation).
Leica Stellaris 5 Confocal Microscope
System: Advanced imaging on a DMI8 base with LAS X Software.
Capabilities:
  Detectors & Lasers: 4 Power HyD® S detectors, tunable White Light Laser (485–790 nm), extended detection to 850 nm, AOBS®.
  TauSense®: FLIM-based photon counting technology.
  Imaging: DIC, fluorescence, color brightfield, and large-scale image stitching with LAS X Navigator.
Zeiss Lightsheet 7 Microscope
Purpose: Fluorescent imaging of live or fixed-cleared whole organisms and organs.
Capabilities: Fast, gentle imaging of living models (e.g., zebrafish, organoids) over time and large cleared specimens with subcellular resolution. Adapts to various clearing methods with specialized optics and sample chambers.
ONi NANOIMAGER
ONi Nanoimager
Capabilities: dSTORM, PALM, PAINT, SPT and smFRET imaging.
Applications: The ONI Nanoimager is used for super-resolution imaging of cellular structures, protein localization, and molecular complexes, as well as single-particle tracking, colocalization analysis, and studying molecular interactions and dynamics in fixed and live cells, including applications in cell biology, neuroscience, virology, and nanotechnology.
SUPER RESOLUTION MICROSCOPY
Alison Margolies
Scientist I
(205) 934-1926
kamargo@uab.edu